System Requirements Specification (SRS)

NanoRiego

# 1. Object & Scope
This System Requirements Specification (SRS) defines the technical and operational characteristics of the NanoRiego irrigation control platform. It captures both the system-level and component-level requirements necessary to fulfill the functionality described in the User Requirements Specification (URS). The SRS acts as a contractual agreement between stakeholders and the development team, serving as a definitive reference for system architecture, implementation, integration, and validation.

# 2. System Overview
NanoRiego is a modular, embedded system for local irrigation automation, consisting of:
- NanoRiegoPCB: Custom PCB integrating microcontroller, RTC, relay interface, and Bluetooth communication.
- NanoRiegoPIO: Embedded software managing irrigation logic, timing, and hardware actuation.
- NanoRiegoAPP: Android application offering real-time user interface and remote operation.
The controller receives user inputs from the mobile interface via Bluetooth and executes real-time irrigation schedules accordingly, while preserving system state during power interruptions.

## 2.1 Hardware Overview
Component	Function	Source	Estimated Cost
NanoRiegoPCB	Central PCB	Custom (MikeMakes)	~10€
Arduino Nano	Microcontroller	Amazon/AliExpress	2€–8€
HC-05	Bluetooth module	Amazon/AliExpress	3€–11€
DS1307 RTC	Real-Time Clock	Amazon/AliExpress	2€–6€
4-Relay Module	Actuation interface	Amazon/AliExpress	2€–8€

# 3. System Requirements
## 3.1 Functional Requirements
- SYS-FR1: The system shall control up to three solenoid valves for water distribution.
- SYS-FR2: The system shall operate one hydraulic pump in tandem with active irrigation zones.
- SYS-FR3: The system shall accept scheduling instructions from the mobile app. Schedule include start time, duration per zone and active days of the week.
- SYS-FR4: The system shall execute scheduled events based on the internal RTC.
- SYS-FR5: The system shall allow manual zone activation via the mobile app.
- SYS-FR6: The system shall store schedule and configuration data persistently.
- SYS-FR7: The mobile app shall enable time/date synchronization and Bluetooth pairing.
- SYS-FR8: The controller shall return current system state upon request.
## 3.2 Interface Requirements
- SYS-IR1: Relay output lines shall switch up to 10A @ 250VAC / 30VDC.
- SYS-IR2: HC-05 module shall operate at 3.3V logic and communicate at 9600 baud.
- SYS-IR3: DS1307 RTC shall communicate via I2C and operate from 5V with backup battery.
## 3.3 Hardware Requirements
- SYS-HR1: The main PCB shall accommodate Arduino Nano, HC-05, DS1307, and relay module via pin headers.
- SYS-HR2: The system shall use a 2-resistor voltage divider to adapt 5V TX to 3.3V RX for HC-05.
- SYS-HR3: All components shall share a common ground or use isolated grounds when necessary.
- SYS-HR4: The pump circuit shall be protected using a DIN-rated auxiliary relay.
## 3.4 Software Requirements
- SYS-SR1: Firmware shall implement a state machine to handle scheduling, manual override, and error states.
- SYS-SR2: Bluetooth parser shall support pairing, command execution, and exception handling.
- SYS-SR3: Mobile app shall be developed using Android Studio and be compatible with Android 7.0+.
- SYS-SR4: EEPROM memory shall be logically mapped for efficient and reliable data retention.
## 3.5 Performance Requirements
- SYS-PR1: System boot time shall not exceed 3 seconds.
- SYS-PR2: Bluetooth reconnection shall occur within 5 seconds.
- SYS-PR3: User input delay shall be under 500 ms.
- SYS-PR4: Time sync error shall remain within ±2 seconds.
## 3.6 Reliability and Safety Requirements
- SYS-RS1: System shall prevent activation of more than one valve at a time.
- SYS-RS2: Pump shall never be active without an open valve.
- SYS-RS3: System shall ignore malformed Bluetooth commands.
- SYS-RS4: UI shall clearly indicate system status and connection health.
- SYS-RS5: Relay modules shall not exceed their rated electrical loads.
## 3.7 Human-Machine Interface
- The application shall present two UI panels:
  - SYS-HMI1: Control dashboard (zone status, timers, manual override, schedule)
  - SYS-HMI2: Configuration page (automatic sync and bluetooth settings)
- SYS-HMI2: All control widgets shall reflect real-time state and enforce logical constraints based on connection status.
# 8. Appendix and References
- Refer to URS Document (v1.0, April 2025)
- GitHub Repository: github.com/MikeMakes/nanoRiego
- Bluetooth Module Datasheet (HC-05)
- RTC Module Datasheet (DS1307)

Revisions to this SRS may be issued upon design iteration or stakeholder feedback.